Principles and practice of gel electrophoresis (polyacrylamide)
Quiz Questions
- Gel electrophoresis separates molecules based on size, charge and shape
- When travelling through agarose gel, larger molecules will migrate slower than smaller products
- DNA has a net negative charge -> travels from the cathode to the anode
- Size of the molecular product is determined by the standard molecular weight ladder
- Buffers utilised instead of water due to the electrolytes, electrically coupling electrodes and migratory biomolecules
Polyacrylamide gel basics
- Tougher than agarose gels
- Very fluid in nature hence preparation occurs between glass/plastic slides for vertical electrophoresis
- Acrylamide monomers link covalently link forming long chains (polymers)
- Polymers covalently linked to other chains with cross linkers
- Gelation a chemical process -> cannot heat up to reform liquid
Major advantages of polyacrylamide gel
- Smaller pores than agarose therefore have a higher degree of resolving power
- Resolving power allows separation of DNA fragments differing by a single nucleotide
- Can be utilised for both DNA and proteins
- Polyacrylamide also chemically inert, ensures no reaction with any biomolecules
- Completely transparent therefore the visualization is very good
Rod or slab gels
- Flat slab gels formed between glass plates -> utilised for vertical electrophoresis
- Rod gels made in narrow bore tubes
- Slabs save time -> 25 samples can be separated under identical conditions
- Rod gels allow for electrophoresis of only a single sample
Protein electrophoresis
General Characteristics
- Proteins separated based on molecular weight
- Allows us to characterize proteins, quantify concentrations, determine the sample purity (i.e. how many bands present), compare proteins from different sources (proteins in human serum vs horse serum)
- Protein electrophoresis is also a step in the western blot (discussed later)
- Unlike DNA, proteins don’t have constant size to charge ratio -> both positive and negative regions
- For proteins particularly we assess non-dissociating (native PAGE) or dissociating electrophoresis (SDS-PAGE)
Native/non-dissociating electrophoresis
- No detergent utilised, ensures proteins remained in their natural state
- Proteins remain in their native/folded state
- Native Page -> separates folded proteins, proteins-protein and protein-ligand complexes by: size, charge and shape
- Native page doesn’t provide direct measurement of molecular weight, technique provides useful information such as;
1. Protein charge (not seen in SDS page)
2. Subunit composition (degree of folding for example)
- Native page can also separate proteins of identical molecular weight -> cannot be done in SDS Page
- Separation of proteins of identical molecular weight -> based on molecular shape (globular or fibrous)
SDS PAGE
- SDS = sodium dodecyl sulphate
- The purpose of the method is to separate proteins solely based on size and no other physical features
- All proteins essentially negatively charge -> the charge is now a function of protein size hence size = major separation factor
- Recall the SDS is negatively charged an initially utilised to chelate Mg2+ stopping the function of DNAase

In depth assessment of SDS-PAGE
Understand two halves -> SDS and then PAGE
SDS -> sodium dodecyl sulphate
- SDS is a detergent -> it is amphipathic
- Amphipathic -> the detergent has both polar + non-polar regions disturbing aqueous polarity around other amphipathic structures
- Detergents therefore degrade cell membranes
- SDS negatively charged -> strong enough to solubilize cell membranes + proteins
- Solubilize = break down the structure
- Proteins treated with SDS -> covered with many negative charges -> proteins will be completely negative essentially
- Why utilise treat proteins with SDS:
- Mass, shape + charge of biomolecules determine how well they move through polyacrylamide
- We try to separate variety of proteins of a variety of charge, shape and size -> we want proteins to be linear + have identical charge
- We utilise SDS to denature all proteins into primary structure -> all proteins linear
- All proteins linear with negative charge -> basis of separation is size
To fully linearize the proteins we do the following:
- Proteins boiled in SDS and beta-mercaptoethanol
- SDS + boiling -> fully disrupts secondary + tertiary structure -> proteins reduced to primary structure
- Mercaptoethanol reduces disulphide bonds -> these are covalent + strong and part of secondary structure
- All linear proteins = negatively charge -> migrate to positive anode
- Migration inversely proportional to linear size
- Molecular weight with respect to size markers may now be utilised -> migration dependant on size -> no shape effects (fibrous/globular)
- The negative charge per unit length of protein constant -> migration solely dependant on protein size
PAGE -> polyacrylamide gel electrophoresis
- PAGE -> preferred method for protein separation
- Formation of PAGE = chemical reaction -> once formed cannot be unformed
- Agarose gel can be heated in microwave in presence of errors -> PAGE needs to be re-prepared
- Preparation of the polyacrylamide gel:
- Polymerization of acrylamide requires the combination of acrylamide, ammonium persulphate and N,N,N’,N’-tetramethylenediamine (TEMED)
- TEMED catalyses the conversion of persulphate ion to give the sulphate radical
- S2O82- + TEMED -> SO41- + SO42-
- The sulphate anion with a negative 1 charge is the radical eliciting polymerization
- The cross-linking of these acrylamide polymers occurs in the presence of N,N’-methylenebisacrylamide (bis-acrylamide)
- Bis-acrylamide essentially polymerises with acrylamide forming cross-links between acrylamide chains
- These cross links are the “pores” that biomolecules pass through
- Pore size in gels varies with varying acrylamide-bisacrylamide ratios
- Polyacrylamide gel preparation -> include all essential components previously discussed
- Acrylamide and bisacrylamide
- 1M tris-HCl solution of pH = 8.8
- Distilled water
- 10% SDS
- 10% Ammonium Persulphate
- TEMED (added last)
1. Mix the ingredients gently, in order of above -> ensure no bubbles
2. Pour into glass plate carefully -> ensure no bubbles
3. Overlay gel with isopropanol -> ensures flat surface + ensures no contact with air
4. Wash off isopropanol with water after gel has set -> +/- 15 minutes
Care with gel preparation:
- TEMED added last since it elicits polymerization -> elicits formation of persulphate radicals (SO41-)
- Isopropanol addition essential -> O2 reacts with free radical SO41- therefore inhibiting polymerization
- O2 may also oxidise protein products -> products cannot be extracted for assessment
Overall assessment of system components
- DC power source, Tank, Glass tank, spacers, combs
- Polyacrylamide gel
- Buffer system with high buffer capacity
- Biomolecules to be separated (Nucleic acids or proteins)
Overall procedure to follow
- Prepare polyacrylamide gel -> in order as stated
- Add diluted biomolecules to sample buffer (containing SDS and mercaptoethanol -> functions discussed)
- Heat to 95 for 4 minutes -> left with negatively charged linear proteins
- Load samples on polyacrylamide gel
- Run @ 150V for 30-40 minutes
- Stain
Continuous and non-continuous buffer systems
 Continuous buffer system
- Consists of only a single separating gel
- The gel is of consistent concentration -> pore size consistent
- Same buffer solution utilised in buffer reservoirs + gel
- The pH in the buffer reservoir + gel is consistent
Discontinuous buffer system
- Non-restrictive stacking gel layered on top of the separating gel -> contrast to continuous buffer system -> gel consistent
- Discontinuous systems also have different buffers in the buffer reservoirs and gel
- Difference in buffers -> buffer components and pH
- The resolution obtainable in discontinuous buffer system -> superior to continuous buffer system -> continuous system easier to set up though
Assessment of discontinuous buffer system functionality
Break discontinuous system into 4 parts:
1. Electrode buffer -> Tris-Glycine (pH 8.3), biomolecule samples loaded into wells here
2. Stacking Gel Buffer -> Tris-HCl (pH 6.8), non-restrictive large pore region
3. Running Gel Buffer -> Tris-HCl (pH 8.8)
4. Electrode buffer -> Tris-Glycine (pH 8.3)
- Essential indirect interaction between glycine ions and chloride ions
- Proteins concentrated into narrow zone allowing formation of sharp protein bands in the “running gel” region
- Biomolecule sample loaded into wells -> large pore stacking buffer allows easy movement of these biomolecules
- Glycine ions move from pH 8.3 to pH 6.8 in stacking gel buffer behind biomolecules where they become zwitterions -> exist as zwitterions along the length of the running gel
- The loss of charge -> glycine moves slowly in the electric filed
- Chloride ions move slightly faster
- Biomolecules (proteins) sandwiched between glycine + Cl- grouping proteins together -> high protein density
- As proteins get separated sharp bands form as they don’t diffuse around -> sandwiched btw 2 ions fronts
Components of continuous sample buffers
- SDS -> ensures proteins denatured with negative charge (SDS included in gel preparation too)
- Mercaptoethanol -> breaks disulphide bonds (included in previous system components too)
- Tris -> provides appropriate pH (vary with use of HCl)
- Glycerol -> ensure the samples sink into the well -> weigh biomolecules down
- Bromophenol Blue -> not a stain, it’s a dye allowing for monitoring of electrophoretic progression
NB: various loading dyes available -> they all have same function of weighing the biomolecules down into the well

Post-electrophoretic procedures
Staining proteins in gels
- Detect proteins based on differential binding of the stain by protein molecules and the gel matrix
- Stains are non-specific -> detecting proteins without regard to their individual identities
- Background staining of the gel occurs -> difficult to assess the bands of proteins
- Destaining can be performed -> removal of background colour
- To destain -> transfer gel to mixture of water + isopropanol + acetic acid and allow to stand for 48h
- Increase destaining process by changing solution constantly
- Coomassie blue -> popular staining agent which is anionic (negatively charged)
- Coomassie blue binds to proteins via:
1. Ionic interactions: negative dye sulfonic acid groups and positive protein amine groups
2. Interactions occur through Van der Waals forces too
- Electrophoretic destaining can be performed with Coomassie blue
- Important characteristics of useful stains:
1. Low background colouration -> little electrostatic interaction with support medium
2. High sensitivity -> detects low concentration of biomolecule
3. Large linear range
4. Ease of use
Determining molecular weights of proteins by SDS-PAGE
- Run gel with proteins of known molecular weights along with protein to be assessed
- Linear relationship exists btw log(Mr) verses relative migration (RF value)
- RF = ratio migrated of biomolecule to that migrated by the dye front (such as bromophenol blue)
- 2 (biomolecule) / 10 (dye front) = 1/5
- Standard curve plotted for standard proteins of known molecular weights
- RF of polypeptide calculated in same way and interpolated off the graph to find log(Mr) -> calculate Mr now
- Appreciate that this applies only to SDS-PAGE -> proteins linear -> separation based on size -> greater log(Mr) smaller RF
Blotting
- Blotting = transfer of separated biomolecules (nucleic acids/proteins) from gel to thin sheet -> nitrocellulose membrane
- Biomolecules bind to membrane + are immobilised
- Blotting of proteins + nucleic acids can be done by electrophoretic transfer -> referred to as western blotting
- ADVANTAGE WESTERN BLOTTING: immobilised proteins on nitrocellulose surface readily accessible to detection reagents + staining and destaining
- Labelled antibodies to detect proteins (immuneblotting) is possible
- Transfer of nucleic acids can be done by electrophoresis (western blotting), southern blotting or by capillary
Isoelectric point and isoelectric focusing
- Isoelectric point = pH at which protein exists as a zwitterion
- pH above pI -> protein negatively charged and migrates towards positive anode
- pH below pI -> proteins positively charged and migrates towards the negative cathode
- Isoelectric focusing = proteins separated in a pH gradient according to their isoelectric points
- Isoelectric focusing occurs in two stages:
1. The pH gradient is formed along the polyacrylamide gel
2. Proteins placed in the centre of the gel and migration begins towards anode or cathode -> when reaching its pI in the pH gradient it becomes a zwitterion and stops migrating
- This is a form of non-dissociating conditions -> no SDS added -> proteins migrate in their native form -> migration based solely on initial charge + pI
- Different proteins will have different pI hence isoelectric focusing is an appropriate separation mechanism
- Iso = same
Limitations of SDS-PAGE or Isoelectric focusing
- 20 – 30 proteins can be separated at a time
- Possibility of some proteins having identical pI (isoelectric focusing) or size (SDS-PAGE)
- Generally, proteins mixtures consist of 2000 – 3000 proteins
Solutions to these limitations:
- Combination of SDS-PAGE and Isoelectric focusing (both 1D mechanisms)
- The technique = 2D electrophoresis
- O’Farrell 2D Gel System
- 2D gel electrophoresis used to separate complex mixtures of proteins into more component mixtures of similar proteins
- Analysis of 2D gels more complex than 1D gels -> no bands -> spots with (x;y) coordinates
- Each dimension separates proteins on different properties:
1. First dimension tube gel is electrofocused (IEF) -> charge and pI is basis of separation
2. Second dimension is an SDS slab gel -> size is the basis of separation
In-depth western blot assessment
- Western blotting = detection technique combining separation power of SDS and together with recognition specificity of antibodies
- Antibodies can be obtained in two ways:
1. From animals immunised with the required antibodies
2. Purchased from a commercial source
Western blotting then occurs in four major steps:
1. Separation of proteins using SDS page
2. Transfer of protein bands onto a nitrocellulose membrane -> proteins immobilised here (blotting process)
3. Immune reaction -> anti-body interaction with the protein
4. Visualization
NB: refer to final page of electrophoresis notes for summary of functions